## Slide 1: Driver Drowsiness Detection System
Mid project presentation

## Slide 2: Why do we need?
“Driver Drowsiness Detection is a vehicle safety technology to help prevent accidents caused by
driver drowsiness”
National Highway Traffic Safety Administration – one million crashes involve drowsy driving a year (NSC)
AAA Foundation for Traffic Safety – 328,000 drowsy crashes every year (NSC)
Lack of a real time monitoring system costs precious lives, costs $109 billions (NSC)
Effective utilization of valuable resources
Safety, comfort and confidence
Notes: Give examples of inspecting driver before (s)he takes over but during journey gets tired due to physical or mental disturbances. So is the need for continuous monitoring in place.
Save Government precious resources such as money, time, police, rescue team, infrastructure, etc. Insurance companies can use funds to natural calamities, or on unforeseen incidents rather than human mistakes
Motor vehicle operators can assure safety, comfort and confidence to passengers
Give examples of inspecting driver before (s)he takes over but during journey gets tired due to physical or mental disturbances. So is the need for continuous monitoring in place.
Save Government precious resources such as money, time, police, rescue team, infrastructure, etc. Insurance companies can use funds to natural calamities, or on unforeseen incidents rather than human mistakes
Motor vehicle operators can assure safety, comfort and confidence to passengers

## Slide 3: Why do we need?
Solutions include
  - Steering pattern monitoring
    Monitors power steering
    Exception - Automatic lane-keeping system
  - Vehicle position lane monitoring
    Uses lane monitor camera
    Exception – Automatic lane-keeping system
  Physiological measurement
    Employs body sensors to measure brain activity, heart rate, muscle activity, etc.
    Relatively expensive
  Driver face monitoring
    Monitors driver face using computer vision with camera
    Simple and affordable
Notes: Give examples of inspecting driver before (s)he takes over but during journey gets tired due to physical or mental disturbances. So is the need for continuous monitoring in place.
Save Government precious resources such as money, time, police, rescue team, infrastructure, etc. Insurance companies can use funds to natural calamities, or on unforeseen incidents rather than human mistakes
Motor vehicle operators can assure safety, comfort and confidence to passengers

## Slide 4: Current Systems in use
Audi – Rest recommendation system
BMW – Active driving assistant
Bosch – Driver drowsiness detection
Ford – Driver alert
Honda – Driver attention monitor
Hyundai – Driver attention alert
Jaguar – Driver fatigue alert

## Slide 5: Why did we pick present solution ?
A system works and continues to work smooth only when it is monitored continuously, and effective, corrective measures take place in time
Studies have shown strong correlation between fatigue and facial expressions and monitoring facial expression is a widely accepted method for detection driver drowsiness.
Drowsy Driving Prevention Week is Nov. 1-8, 2020 (https://www.nsc.org/road-safety/safety-topics/fatigued-driving)

## Slide 6: Project objectives
Detecting fatigue and drowsiness levels
Study the requirements of problem
Research solutions, merits and demerits
Analyze feasibility and applicability
Prepare a cost-effective fool proof driver alert system

## Slide 7: Project scope
Functionality scope
  Affordable by all vehicles
  Automatic reporting to vehicle operators
  Avoid major catastrophe
Technical scope
  Supervised / Unsupervised
  Machine learning / Deep Learning
  Hybrid machine learning / Ensemble approach
  Intelligent systems / Sense making systems
Notes: Several solutions exist. Majority are employed in luxury vehicles. Life is precious and not to be scaled based on money alone. Who knows the poor guy travelling in a passenger vehicle is not Einstein?
In case, the driver is less fatigue and controls - even then the reports can be captured appropriate safety precautions can be taken by the operators in time.
In case, the driver is in helpless state – advance sensor controls can rescue by leaving the vehicle to a stable state keeping the circumstances in view.
- at least can alert passengers inside so that they can take appropriate measures (if such costly equipment is not administered)

## Slide 8: Data resource required
Images of face with open and closed states of left and right eyes |  | 
Eye image data bank: | Attributes | 
http://mrl.cs.vsb.cz/eyedataset | Subject | Identifies subject
 | Image | Identifies image
 | Gender | Man / Woman
 | Spectacles | Wears or not glasses
 | Reflections | No / small / big reflections
 | Lighting conditions | Good / Bad light condition
 | Device sensor | Sensor captured image
 | Eye state | Closed / Open state of Eye

## Slide 9: Data resources
Images of face with open and closed states of left and right eyes
The eye image data bank
  http://mrl.cs.vsb.cz/eyedataset

## Slide 10: Bird eye view
Image collection
Folder Structure
http://mrl.cs.vsb.cz/eyedataset
Image Acquisition
Feature Extraction
Knowledge
Training Data
Validation Data
Image Acquisition
Feature Extraction
Matching
Open
Closed

## Slide 11: Detailed look at the model

## Slide 12: Another view
Collect eye
images
Train
Deep Learning
Get optimal weights
Read Image
Predict eye status
Open
Closed

## Slide 13
Haar features to detect face features like eye, nose, mouth, etc.
Etc.
Haar features are named after Alfred Haar,
a Hungarian mathematician.
Viola and Jones have defined several Haar like features to
detect facial parts from an image.
For example,
can detect eye-brows of a person.
can detect nose portion of a person.
Extended
Haar like features
Original
Haar like features
Edge Features
Line Features
Center Surround Features

## Slide 14
https://www.youtube.com/watch?v=F5rysk51txQ&ab_channel=GlobalSoftwareSupport
Facial feature detection technique
The gray scale image will have pixel values ranging from 0 through 255.
This haar cascade classifier detects darker eye-brows and lighter
forehead.
This haar cascade classifier detects lighter nose and darker
side regions.
This haar cascade classifier detects darker upper and lower
lips differentiating brighter teeth region.

## Slide 15
255 | 254 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
254 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 250 | 253 | 255 | 251 | 255 | 254 | 253 | 255 | 255 | 255 | 253 | 255
54 |  | 88 | 135 | 187 | 243 | 253 | 255 | 253 | 253 | 253 | 252 | 253
 | 0 |  |  | 0 |  | 22 |  | 91 | 154 | 219 | 252 | 254
47 |  |  | 1 |  |  | 0 |  |  | 6 |  | 52 | 141
211 | 148 |  | 76 |  | 13 |  |  | 0 |  | 15 | 101 | 195
248 | 252 | 255 | 254 | 255 | 230 | 156 |  | 52 |  |  | 0 | 
254 | 252 | 255 | 248 | 252 | 249 | 255 | 230 | 220 | 203 | 107 |  | 14
130 | 167 | 236 |  | 68 | 245 | 255 | 252 | 255 | 253 | 255 | 245 | 141
149 | 252 | 122 | 131 | 247 |  | 41 | 242 | 255 | 253 | 255 | 249 | 255
251 | 255 | 110 | 158 | 255 | 124 |  | 97 | 238 |  | 35 | 239 | 254
27 |  | 73 | 253 | 249 |  | 44 | 182 | 255 | 129 |  | 67 | 212
A portion of graphic gray color image with intensity values in numeric form

## Slide 16
How are we using Haar features?
Let us see how it is going to work taking a small nose portion of the image.
Ideal Haar feature pixel intensities
  0: white
  1: black
Real intensity values of nose portion
0.9 | 0.2 | 0.1 | 0.1 | 0.1 | 0.2 | 0.3 | 0.9
0.8 | 0.2 | 0.1 | 0.1 | 0.1 | 0.2 | 0.3 | 0.8
0.6 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.2 | 0.6
0.6 | 0.1 | 0.2 | 0.2 | 0.2 | 0.1 | 0.1 | 0.6
0.6 | 0.1 | 0.2 | 0.2 | 0.2 | 0.1 | 0.1 | 0.6
0.6 | 0.1 | 0.2 | 0.2 | 0.2 | 0.1 | 0.1 | 0.6
0.6 | 0.1 | 0.2 | 0.2 | 0.2 | 0.1 | 0.1 | 0.6
0.6 | 0.1 | 0.2 | 0.2 | 0.2 | 0.1 | 0.1 | 0.6
That’s lot of computations. Is there a way we can reduce ?

## Slide 17: Simplification through Integral summation
As we saw in previous slide, for various image sizes, we need to compute the sums. Viola – Jones have found a simple technique using which we can compute sum of any co-ordinate (x, y) with just 4 values.
Let us explain this with an example:
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
1 | 2 | 3
2 | 4 | 6
3 | 6 | 9
Input Image
Integral sums

## Slide 18
0.9 | 0.2 | 0.1 | 0.1 | 0.1 | 0.2 | 0.3 | 0.9
0.8 | 0.2 | 0.1 | 0.1 | 0.1 | 0.2 | 0.3 | 0.8
0.6 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.2 | 0.6
0.6 | 0.1 | 0.2 | 0.2 | 0.2 | 0.1 | 0.1 | 0.6
0.6 | 0.1 | 0.2 | 0.2 | 0.2 | 0.1 | 0.1 | 0.6
0.6 | 0.1 | 0.2 | 0.2 | 0.2 | 0.1 | 0.1 | 0.6
0.6 | 0.1 | 0.2 | 0.2 | 0.2 | 0.1 | 0.1 | 0.6
0.6 | 0.1 | 0.2 | 0.2 | 0.2 | 0.1 | 0.1 | 0.6
0 | 0 | 1 | 1
0 | 0 | 1 | 1
0 | 0 | 1 | 1
0 | 0 | 1 | 1
0.9 | 1.1 | 1.2 | 1.3 | 1.4 | 1.6 | 1.9 | 2.8
0.8 | 2.1 | 2.3 | 2.5 | 2.7 | 3.1 | 3.7 | 5.4
2.3 | 2.8 | 3.1 | 3.4 | 3.7 | 4.2 | 5.0 | 7.3
2.9 | 3.5 | 4.0 | 4.5 | 5.0 | 5.6 | 6.5 | 9.4
3.5 | 4.2 | 4.9 | 5.6 | 6.3 | 7.0 | 8.0 | 12
4.1 | 4.9 | 5.8 | 6.7 | 7.6 | 8.4 | 9.5 | 14
4.7 | 5.6 | 6.7 | 7.8 | 8.9 | 9.8 | 11 | 16
5.3 | 6.3 | 7.6 | 8.9 | 10 | 11 | 13 | 18
1.1
1.1 = (8.4 + 2.5) - (6.7 + 3.1)
Viola – Jones simplification of Summation to just 4 value addition
Source - https://www.youtube.com/watch?v=p9vq90NYHMs&ab_channel=YoussefShakrina
Integral Image
Original Image
The simplification reduces the huge number of calculations drastically.

## Slide 19
Pretend 3 Haar like features to capture eyes, nose, mouth.
Note:
(For simplicity, we are showing image scanning with fixed filter size but in reality it will be done at multiple scales.)
A
Let us watch the algorithm visually
No Match!
Found Match!

## Slide 20
Edge detection Filter technique to highlight horizontal and angled lines and lower importance of vertical lines

## Slide 21
Pretend 3 Haar like features to capture eyes, nose, mouth.
A
Let us watch the algorithm visually
No Match! Scan next one.
Found Match!

## Slide 22
Let us watch how the first kernel (haar like edge detection) slides
Let us watch the second kernel (haar like edge detection) slides

## Slide 23
Let us see how pattern matching works
.1 | .1 | .1 | .1
.1 | .1 | .1 | .1
.9 | .9 | .9 | .9
.9 | .9 | .9 | .9
Image intensities
Haar like Image
(Sum of dark pixels ~ Sum of bright pixels)/8
= (7.2 – .8) / 8 = 6.4 / 8 = 0.8
Sum of dark pixels – Sum of bright pixels
= 4 – 0 = 4 / 4 = 1
Our task is to compare an image with a Haar like image as shown below:
0 | 0 | 0 | 0
1 | 1 | 1 | 1
i.e. the image matches by 80%
Image intensities
.9 | .1 | .9 | .1
.1 | .9 | .1 | .9
.9 | .1 | .9 | .1
.1 | .9 | .1 | .9
(Sum of dark pixels ~ Sum of bright pixels)/8
= (4 – 4) / 8 = 0 / 8 = 0
i.e. the image doesn’t match with the pattern.

## Slide 24
Our Approach
A neural network model with no hidden layer can represent a linear function or decision.
A feedforward network with a single layer is sufficient to represent any function, but the layer may be infeasibly large and may fail to learn and generalize correctly.
— Ian Goodfellow, DLB
So, we’ve decided to create two models:
  first model with a pair of Convolution and MaxPool layers
  second model with three pairs of Convolution and MaxPool layers
Common layers:
  Dropout to prevent overfitting
  Flatten layer to step down dimensions
  Dense for Full connectivity
Study if increase of layers would have any impact in accuracy.
Model - I
Model - II

## Slide 25
Results of running models
Addition of two more pairs of Convolution and MaxPool layers has no remarkable improvement in performance. It has tripled the execution time.
We could satisfy and stop with Epochs = 15

## Slide 26
Other techniques that boost the algorithm
The algorithm discards the sub images of the given image soon after it finds none of the patterns
i.e. with low probabilities or matching quotient.
It assembles several weak classifiers to become a strong classifiers.
In summary, the algorithm works wonders on real world scenarios through effective use of
Integral Summary
Adaboost Ensembling weak classifiers to build a strong classifier
Utilization of Haar like features

## Slide 27: Extensions
Given appropriate training data, the model can be extended to capture not only the status of eyes but also the feelings.
Source - https://www.doc.ic.ac.uk/~jam414/AffectiveComputing/anmol.html

## Slide 28: Accomplishments
Survey of various techniques employed in real world
Study on capturing video, image processing using OpenCV
Applied knowledge gained from Singapore National University lectures
References
  https://www.superdatascience.com/blogs/opencv-face-detection
  https://machinelearningmastery.com/how-to-perform-face-detection-with-classical-and-deep-learning-methods-in-python-with-keras/
  https://towardsdatascience.com/real-time-face-recognition-an-end-to-end-project-b738bb0f7348
  https://docs.opencv.org/3.4/db/d28/tutorial_cascade_classifier.html
  Data set - http://mrl.cs.vsb.cz/eyedataset

## Slide 29: Limitations & Improvements
Limitation – Assumes driver wears transparent glasses (not dark glasses obstructing structure of eye)
No matter how many advances, precautions we take we also know how to brake. After all we human intellectuals make and break!
Future Scope
  Driver obstructing the monitoring system
  Address eye blink rate
  Yawning
  Missing turns or exits
  Addressing low light conditions
  Address reflections
Notes: Each person may have different blink rates, so system can be trained to capture and predict accordingly.
Device capturing images of drivers’ face wearing spectacles may have reflections; system can be trained considering such images to address such conditions

## Slide 30: Thank you
Singapore National University
Professors for imparting knowledge
Administrative staff

## Slide 31
Questions and Comments